## Slide 1: CS118 Assembly Language
Chapter 2
Major Components of Computer “Engines”

## Slide 2: Section 1
Understanding the Limits of Portability

## Slide 3: Hardware Components of Computers
This chapter is about the components of computers
We will study the internals of the computer
Keep an eye out for how the components contribute to speed

## Slide 4: Portability
In programming classes, portability is a big consideration
Java is a very portable language due to the JVM
C++ is mostly portable, but there are several add-ons that are not portable

## Slide 5: Examining Portability: The Software Viewpoint
For most programming languages, portability is a serious consideration
By portability, we don’t mean that the language itself is portable
We mean that programs written in the language are portable

## Slide 6: Operating Systems
Most operating systems are written for a specific piece of hardware
This is because the operating system has to work with the hardware
  Different hardware operates (at a low level) in different ways
Operating systems are written by people and different people think differently

## Slide 7: Specific Operating Systems
From the book:
“A program written to work on a PC under the Windows OS will probably not run on the same machine under the Linux OS (and vice versa), since the program will probably call operating system functions”

## Slide 8: Examining Portability: The Hardware Viewpoint
Programs are almost never portable across different hardware
IBM PCs are upward compatible
  This means that programs designed for Pentium hardware still run on today’s machines

## Slide 9: Portability Across Different Microprocessors
This is almost always impossible
Programs written for Motorola hardware will not run on Intel hardware

## Slide 10: Section 2
Examining Hardware

## Slide 11: Memory 01

## Slide 12: Memory-Just Chips
Memory is just a series of chips
We know that what is stored there is temporary
  If the CPU loses power, memory loses its contents
However, memory should be viewed like a long array of bytes

## Slide 13: The Term Memory
As the book suggests, many (non-technical) people confuse memory and disk storage
They are very different

## Slide 14: Memory vs. Other Storage
Memory is just a series of chips
The disk has a spinning “platter” inside it
Memory is volatile
A disk stores data permanently
Memory is super fast
A disk is a very slow storage device

## Slide 15: Vocabulary: Reading and Writing
Getting data from a device is called reading the data or reading from the device
Sending data to a device is called writing the data or writing to the device
  Of course, you write to a device because you want to change data
  So, writing data often means changing the data

## Slide 16: Connecting the CPU and Memory
The wires connecting the devices are called buses
  There is a data bus
    The CPU sends data to memory or retrieves data from memory on this bus
  There is an address bus
    The CPU uses this to tell memory where to store the data or get it from
  There is a control bus
    The CPU uses this to tell if it’s reading or writing

## Slide 17: I/O Devices 02

## Slide 18: I/O Devices
The CPU has a lot of other devices connected to it
The purpose of most of them is to
  Get data from us, and
  Make answers available to us
These are called I/O devices
  I/O means input/output
Examples are printers, keyboards, mice

## Slide 19: Nothing Ever Changes
We use the same vocabulary (reading, writing) when talking about devices
We also have buses connecting the devices
This is very similar to how the CPU and memory are connected

## Slide 20: The CPU 03

## Slide 21: Inside the CPU
In the last chapter, I mentioned several components of the CPU
I want to look at them in more detail

## Slide 22: The ALU
This is the part of the CPU that does math and other similar operations
If you need to add 2 and 3, the CPU does that
It has to store its answers somewhere, though

## Slide 23: Registers 04

## Slide 24: Hex Digits And Bytes
Notice that
  A byte is eight bits
  One hex digit is four bits
This means there are two hex digits in a byte
Some people call one hex digit in a byte a nibble 

## Slide 25: Registers
Registers are storage places inside the CPU
  That makes it fast to store data or retrieve data from them
The registers are broken down by their sizes

## Slide 26: General Purpose Registers
8 bit registers: al, bl, cl, dl
More 8 bit registers : ah, bh, ch, dh
16 bit registers : ax, bx, cx, dx
32 bit registers : eax, ebx, ecx, edx
64 bit registers : rax, rbx, rcx, rdx

## Slide 27: A Picture
Remember this picture and its b, c, d, versions

## Slide 28: Checking That Picture
Wait!
Are you telling me that ah is inside ax?
Yes, yes, and yes
  Oops. There was only one question 
So, also, ax is part of eax, etc., according to what you see in the picture
This takes some getting used to

## Slide 29: Testing This Idea
Suppose I execute the (fake) instruction
  STORE 2234323416 INTO eax
What is in ah?
What is in al?
What is in ax?
What is in eax? (obvious question)
What is in rax? (trick question?)

## Slide 30: Special Purpose Registers
The PC
  The program counter
  Holds the address of the currently executing instruction
The IR
  The instruction register
  Contains the currently executing instruction itself

## Slide 31: More Special Purpose Registers
EFLAGS
  This is also called the processor status register
  There are individual flags (indicators) to tell if the result of the last calculation was 0, negative, etc.
ESP
  The stack pointer
  Points to a stack in memory

## Slide 32: Still More Special Purpose Registers
MAR
  The memory address register
  It’s where the CPU puts a data address to read or write
  Connected directly to the address bus
MDR
  The memory data register
  It’s where the CPU puts data or gets data that is transferred to/from memory
  Connected directly to the data bus

## Slide 33: The Instruction Cycle 05

## Slide 34: Executing Instructions
Here are the steps the CPU goes through to process one instruction
There are four steps
They are
  Fetch the current instruction from the address pointed to by the PC
  Update the PC to point to the next instruction
  Copy the instruction to the IR
  Execute the instruction in the IR

## Slide 35: Step 1: Fetch an Instruction from Memory
The CPU copies the PC to the MAR
The CPU reads memory
The contents of memory is then in the MDR

## Slide 36: Step 2: Update the PC
The PC is incremented to point to the next location in memory

## Slide 37: Step 3: Copy the Instruction
The instruction is copied from the MDR to the IR
The instruction in the IR is decoded

## Slide 38: Step 4: Execute the Instruction
The instruction is then executed
This may involve more memory access
For example, if the instruction is
    movw x,%ax
then execution will require getting the contents of x

## Slide 39: Repeat, Repeat, Repeat
The CPU just repeats this cycle over and over again
As the book says, this is done by the hardware
  It’s very easy
  The same process is used over and over again
  That’s ideal for the hardware

## Slide 40: Speeding up the Process 06

## Slide 41: Pipelining
We can execute the next Copy instruction while the executing the previous Fetch instruction
This is called pipelining
It’s also referred to as parallel architecture

## Slide 42: Superscalar Hardware
Some machines have multiple ALUs
This is another way to speed up a processor

## Slide 43: Other Techniques
There are other techniques that are used to speed up instruction execution

## Slide 44: Multiprocessors
It’s very common to have more than one CPU inside of a processor chip
Common processors today have 2, 4, or 8 CPUs inside

## Slide 45: The Clock Cycle
There is a clock that controls CPU speed
It is like a metronome used in music
It goes tick, tick, tick, …
The processor can do one step in every tick
Most instructions take multiple steps

## Slide 46: The Clock Speed
If a CPU runs at one gigahertz, it has one clock tick every billionth of a second
  Hertz means once per second
  Giga means a billion or 109
Common speeds today are 3-4GHz

## Slide 47: Cache 07

## Slide 48: Cache
Cache is a small amount of memory inside the CPU
It has very quick access since it’s inside the CPU
Getting to memory is hard and takes time
  The bus is slower
  There is often bus overhead

## Slide 49: The Idea behind Cache: No Cache
Scenario 1: No cache
  You have a while loop in a program
    while (item_count != 0)
    {
    }
Evert iteration of the loop requires a memory access to x

## Slide 50: The Idea behind Cache: With Cache
The first time the CPU executes the loop, it copies item_count to cache
The cache keeps track of whether item_count changes
  This is quite easy and takes no time
Now, the loop runs faster, since the CPU only accesses cache, not memory

## Slide 51: Storing Memory Values in Cache
Memory is broken into blocks
The cache can hold several blocks
  A storage area in cache that can hold a block is called a line
The cache knows which block is stored in which line

## Slide 52: Speed and Cache
So, instead of accessing actual memory, the CPU only accesses cache
If the CPU needs a byte not in cache
  The cache finds an open line
    If there’s not an open line, the cache evicts a block of memory
  It then reads the correct block into cache
  It also notes which block went into the line

## Slide 53: The CPU and Cache
The CPU is pretty clueless
It talks to the cache
Cache talks to memory
The CPU reads and writes to cache
  It thinks cache is memory
It lets cache manage itself

## Slide 54: Changing Memory
What if the CPU wants to change the value of a byte in memory?
The CPU just tells the cache to change the value of the byte
How should the cache respond?
  The CPU thinks the byte is in memory
  The cache knows it’s only in cache

## Slide 55: Write-Back and Write-Through
There are two strategies
One is write-back
  The cache only writes to memory when it evicts a block
  It writes an entire block
The other is write-through
  Every time the cache changes a byte, it also changes that byte in memory

## Slide 56: Comparing the Techniques-Part 1
Write-through can be a time waster
  Look at this loop
    int sum = 0;
    for (int i=0; i<10000; i++)
    sum += i;
  Every iteration changes sum
  We only care about sum after the loop
  sum is being written back to memory on each iteration

## Slide 57: Comparing the Techniques-Part 2
Write-back can be a time waster
  Look at this loop
    for (int i=0; i<10000; i++)
    cout << i;
  Every iteration changes i
  When the block is evicted
    The entire block would have to be written
    But, only one byte was changed
  This is bad if the block is written back often

## Slide 58: Choosing
Many CPUs allow a programmer to choose write-back or write-through
In fact, a programmer can even declare parts of memory as non-cacheable

## Slide 59: Other Uses of the Word Cache
There is a similar idea for disks
Disks are slow devices and cache is used to speed them up
There is also a similar idea for the internet
Usually, large amounts of data come in from the internet for each page access
Redisplaying saved data is faster than re-retrieving it

## Slide 60: CREDITS!
CREDITS: This presentation template was created by Slidesgo, including icons by Flaticon, and infographics & images by Freepik.